## Slide 1: Overflow Sensor for ELISA Plate Washer
Jenna Wen
August 12, 2019

## Slide 2
CAD files, circuit diagrams, BOM, and SOP at:
https://github.com/jennaniwens/fiveprime2019-overflow_sensor

## Slide 3: Overview
Added a feature to washing systems to detect liquid overflow and stop washer function
Plate washer with overflow sensor mounted
Overflow sensing module

## Slide 4: Purpose
ELISA plate washers can’t sense liquid spills
Notes: Washer
- Possible interface point is circled

## Slide 5: Overflow Sensing System
Washer is running
Spill occurs
Spill is detected
Washer is turned off
User cleans up spill and restarts washer

## Slide 6: Sensing Circuit & Components
Indicator light states
Varistor placed in parallel with washer to protect it from voltage spike after the machine is reset
Light | Sensor State | Circuit State | Washer State
On | Tripped | Open | Off
Off | Actively Sensing | Closed | On
Flyback diode to dissipate voltage spikes from the relay
Capacitive sensor senses capacitive changes up to 8mm away
DC to AC Relay interface between sensing circuit and washer
Circuit design by Stephen Mehi

## Slide 7: Sensor Mount Considerations
Did not want to drill a hole into plate washer (used existing hole)
Sturdy enough to hold sensor up even when not in use
Intuitive for user to remove and clean

## Slide 8: Things Learned from Overflow Sensor Project
States table (switch etc)
Check Normally Open / Normally Closed states of components
Latching relay wiring
  Translating circuit diagram to electrical component
Prototyping the sensor mount
  Contacted external vendor for machining
SOP-writing
  for resetting, cleaning, and switching out indicator light
  Includes FAQs, wiring details
Indicator light states
Light | Sensor State | Circuit State | Washer State
On | Tripped | Open | Off
Off | Actively Sensing | Closed | On
Stephen Mehi
Notes: Normally open / normally closed
Operates like a switch that’s either open or closed, until it receives an impulse that causes the other switch state
Latch relay wiring
Actual part looks very different from how it’s supposed to be wired